## Slide 1: Lecture 2

## Slide 2
Converting Fractional Parts
  Decimal to binary
    Note: in fractional part, you multiply by 2 instead of dividing.
    (0.6875)10 = (0.1011)2
    (0.6875 * 2) = 1.375, (.375 * 2) = 0.75, (.75 * 2) = 1.5, (.5 * 2) = 1.0
    To check if the answer is correct, apply the polynomial method
  Binary to decimal
    (0.1011)2 = (0.6875)
    (0.1011)2 = 1*2-1 + 0*2-2 + 1*2-3 + 1*2-4
    = (1/2) + 0 + (1/23) + (1/24) = (0.6875)10
  Decimal to hexadecimal
    Note: in fractional part, you multiply by 16 instead of dividing
    (0.0705)10 = (.120C49……..)16
    (0.0705 * 16) = 1.128, (.128 * 16) = 2.048, (.048 * 16) = 0.768, (.768 * 16) = 12.288, (.288 * 16) = 4.608, (.608 * 16) = 9.728 , ……….

## Slide 3
Signed Magnitude Representation of Integer
  Sign Magnitude Representation (S.M.R)
    Sign bit 0 if N >= 0
    1 if N < 0
    Ex 1. represent (+13)10 in S.M.R
    Since (13)10 = (00001101)2,
    When sign bit = 0, that means the number is positive
    Ex 2. represent (-13)10 in S.M.R
    When sign bit = 1, that means the number is negative
    Drawbacks of S.M.R
      Zero has two representations
      Arithmetic involves more steps
0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 1

## Slide 4
  2’s Complement
    There are 2 complement forms for each base “b”
      The b’s complement system: Given N (a positive number) in base b with the non-zero integral part of n digits, the b’s complement is defined as:
        bn – N if N != 0
        0 if N = 0
      The (b-1)’s complement
        Base b’s complement (b-1) complement
        b = 2 2’s complement 1’s complement
        b = 10 10’s complement 9’s complement
        b = 16 16’s complement 15’s complement
        *another way to compute 2’s complement
        1- take 1’s complement: you flip 1’s to 0’s and 0’s to 1’s
        2- add 1’s to it
        Ex. 2’s complement of (10110)2 01001
        Step 1. 1’s complement = 01001 + 1
        Step 2. add 1 to it. = 01010
        01001 + 1 = 01010

## Slide 5
Ex. find the 10’s complement of ( 52520)10
  N = 52520 //the number
  b = 10 // the base
  n = 5 //number of integers
  bn – N = 105 – 52520 = (47480)10
Ex. find the 10’s complement of (0.3269)10
  N = 0.3267
  b = 10
  n = 0
  bn – N = 100 – 0.3267 = (0.6733)10
Ex. find the 10’s complement of (25.639)10
  N = 25.639
  b = 10
  n = 2
  bn – N = 102 – 25.639 = (74.361)10

## Slide 6
Ex. find the 2’s complement of (101100)2
  N = 101100
  b = 2
  n = 6
  bn – N = 26 – 101100
  We must convert 26 from decimal to binary first
  26 = 64 = 01000000
  bn – N = 01000000 – 00101100 = (00010100)2
Ex. find the 2’s complement of (0.0110)2
  N = 0.0110
  b = 2
  n = 0
  bn – N = 20 – 0.0110 = 1.0000 – 0.0110 = (0.1010)2
  ***Subtraction of binary: when u borrow 1, it turns into 2***
  01000000 1.0000
  - 00101100 - 0.0110
  = 00010100 = 0.1010