## Slide 1: Lecture 3

## Slide 2: The (b-1)’s complement
Given a positive number N in base b with the integral part of n digits and the fractional part of m digits, the (b-1)’s complement of N is defined
(bn - b-m ) – N

## Slide 3
Ex. find the 9’s complement of (52520)10
  N = 52520, b = 10, n = 5,
  m = 0 // number of fractional part digits
  (bn – b-m) – N = (105 – 10-0) – 52520
  = (100,000 – 1) – 52520 = (47479)10
Ex. find the 9’s complement of (0.3267)10
  N = 0.3267, b = 10, n = 0, m = 4
  (bn – b-m) – N = (100 – 10-4) – 0.3267
  = (1 – 0.0001) – 0.3267 = (0.6732)10
Ex. find the 9’s complement of (25.639)10
  N = 25.639, b = 10, n = 2, m = 3
  (bn – b-m) – N = (102 – 10-3) – 25.639
  = (100 – 0.001) – 25.639 = (74.36)10

## Slide 4
Ex. find the 1’s complement of (101100)2
  N = 101100, b = 2, n = 6, m = 0
  ( bn – b-m) – N = (26 – 2-0)10 – (101100)2
  = (63)10 – (101100)2 = 111111 – 101100
  OR
  = (1000000 – 1) – 101100 = (010011)2
  Or simply flip 1’s to 0’s and 0’s to 1’s  101100 = 010011
Ex. find the 1’s complement of (0.0110)2
  N = 0.0110, b = 2, n = 0, m = -4
  (bn – b-m) – N = (20 – 2-4)10 – (0.0110)2
  = (1 – 0.0001) – 0.0110 = 0.1111 – 0.0110
  = (0.1001)2

## Slide 5: The Review from the last week

## Slide 6: A quick & easy way to compute 1’s complement and 2’s complement

## Slide 7: Machine Representation of an Integer

## Slide 8: Negative Integers

## Slide 9
Machine Representation of Integers
  Positive integer = Signed Magnitude Representation
  Negative integer = 2’s Complement Form
  byte = 1 byte
  word = 2 byte
  dword = 4 byte
  Ex. Represent (+23)10 in 1 byte
  Ex. Represent (-23)10 in 1 byte
  An overflow occurs when carry- in != carry out
  ex.
  carry-out carry- in
0 | 0 | 0 | 1 | 0 | 1 | 1 | 1
1 | 0 | 0 | 1 | 0 | 1 | 1 | 1

## Slide 10
Ex. 4 bit integers ???????????
  4 0 1 0 0 -4 1 1 0 0
  5 0 1 0 1 -3 1 0 1 1
  -1 1 0 0 1 +7 0 1 1 1
  Carry- in = 1 Carry- in = 0
  Carr- out = 0 Carry- out = 1
  Then, overflow Then, overflow
  -7 1 1 1 1
  -6 1 1 1 0
  1 1 0 1
  Carry- in = 1
  Carry- out = 1
  Then, no overflow exist.
  Arithmetic overflow simply means that the sign bit digit changes between the original and result which gives a different number if treated as a sign bit.